## Slide 1: Dealing with earthquakes and other non-linear motions
T. A. Herring M. A. Floyd
Massachusetts Institute of Technology
GAMIT/GLOBK/TRACK Short Course for GPS Data Analysis
Korea Institute of Geoscience and Mineral Resources (KIGAM) Daejeon, Republic of Korea
23–27 May 2016
Material from T. A. Herring, R. W. King, M. A. Floyd (MIT) and S. C. McClusky (now ANU)

## Slide 2: Outline
Previous lecture showed common time series models
  Linear rate
  Seasonal terms
  Temporally correlated noise
Irregular perturbations to such models include
  Discontinuities due to equipment or environment changes
  Discontinuities due to earthquakes
  Non-linear motions due to earthquakes
  Non-linear motions due to transient events (e.g. volcanic inflation episodes)
Recommended implementation

## Slide 3: Changes to equipment
Antenna is main concern, although receiver may also affect continuity of calculated position
  Even antennas of the same model type may not be manufactured within acceptable geodetic tolerance
stinf_to_rename useful for creating automatic list

## Slide 4: Changes in multipath environment
Photograph by R. Haught
Photograph by R. Haught
Photograph by M. Floyd
Photograph by M. Floyd
Notes: SB4 showing November 2013 fire (http://cdfdata.fire.ca.gov/incidents/incidents_details_info?incident_id=932). GPS antenna (TG01) in upper right.

## Slide 5: Rename scheme
Rename scheme uses first character of suffix
  XXXX_GPS → XXXX_2PS → XXXX_3PS → … etc.
Beyond “9PS”, convert to 10th letter of alphabet (“JPS”) and beyond
  … → XXXX_9PS → XXXX_JPS → XXXX_KPS → … etc.
  But remember “XPS” is a special case for excluding sites from globk runs
For manual renames (e.g. due to manual inspection rather than known events), use 8 available letters in alphabet before “J”
  XXXX_APS, XXXX_BPS, etc.
  But remember “GPS” is a special case (the default)

## Slide 6: Earthquakes
Earthquakes occur at known times
May exhibit more than just a discontinuity
Take care when earthquake occurs in the middle of processing day
  Some data will fall before and some after ground displacement
  Time series point on day of earthquake may appear between pre-earthquake and post-earthquake position

## Slide 7: Radius of influence
eq_def line in eq-file contains earthquake ID (two characters), location, etc.
  ID is used to substitute last two characters of 8-character site name, e.g. XXXX_GPS → XXXX_GSN
sh_makeeqdef will search archives (ANSS ComCat or ISC) to generate eq_def records

## Slide 8: Non-linear motions
Logarithmic decay
Derives from afterslip on fault plane controlled by rate-and-state friction (e.g. Marone et al., 1991)
Velocity perturbation reduces with 1/t
Exponential decay
Derives from assumption of viscoelastic relaxation in stressed medium, e.g. after an earthquake

## Slide 9: Non-linear motions
Logarithmic decay
Exponential decay
Logarithmic looks good in East; Exponential looks good in North; Height doesn’t care

## Slide 10: Many earthquakes…
Complications arise in a tectonically active area with multiple events
Sites may be renamed several times and therefore have various two-character suffixes
Non-linear motions may be included in apr-file with “EXTENDED” records (see globk help)

## Slide 11: Undocumented effects
Time series inspection is very important to catch undocumented effects
Insert manually-determined discontinuities using letter for first character of suffix
? Jump is due to washer removal from top of the antenna.
?
2010-04-04 Mw7.2

## Slide 12: Other phenomena
Several examples of other phenomena some of which are likely to be motions of the monuments (often not tectonic), propagation medium effects, or failed equipment.
With continuous data these types of effects can often be diagnosed from the data.
For artifact effects, multipath and SNR measures are often useful for diagnostics.

## Slide 13: Bombay Beach Creep?
Notes: High light FOGMEX rate sigma (red sloped lines). Vertical rate of El Major Cucapah (2010/04/04)

## Slide 14: Episodic events: Yellowstone
Profile of velocity estimates across region. Large error bars (FOGMEX) show systematic sites
List of noisy sites

## Slide 15: Selected Yellowstone time series

## Slide 16: Episodic Tremor and Slip (ETS): Cascadia
Notes: Annual in height but east is ~14 months (notice offsets move relative to sinusoidal wave).

## Slide 17: Other examples
The following examples are from the UNACVO GAGE Data technical news: http://plus.google.com/u/0/communities/112834235701900858710
Reports here on various anomalies that have been detected and investigated. Useful place to look for site issues.
GAGE ACC quarterly reports also contain information on anomalies

## Slide 18: Local collapse
Site EOCG
http://plus.google.com/u/0/communities/112834235701900858710

## Slide 19: Landslide prone site
Location of earlier landslide showing strong seasonal

## Slide 20: Ground water P271
Site P271 is strongly affected by ground water withdrawal
There are also horizontal periodic signals as well

## Slide 21: Vegetation Growth P158
North (not shown) is less affected.

## Slide 22: Bad antennas
Notes: Red lines are Hector Mine and El Mayor Cucapah.

## Slide 23: Snow on antenna

## Slide 24: Skewed position residuals: Atmosphere delays?
Notes: Site sits near two high volcanoes with a NS valley between the volcanoes.

## Slide 25: Recommendations
Know your goals
  Only fit “nuisance” terms
  It is usually best not to try to fit signals that you are interested in, e.g. seasonal terms if you are studying these.
Depending on your goal (e.g. linear tectonic velocities), sometimes you just have to abandon data as it is likely to do more harm than good (rename to xxxx_XPS or xxxx_XCL). Adding large process noise in GLOBK is one approach but be careful not to make too large. GLOBK sig_neu command can be used for small duration “bad” events.