## Slide 1: GAMIT/GLOBK for GNSS
T. A. Herring1 M. A. Floyd1 M. Perry2 1Massachusetts Institute of Technology, Cambridge, MA, USA 2University of Montana, Missoula, MT, USA
GPS Data Processing and Analysis with GAMIT/GLOBK and track Hotel Soluxe, Bishkek, Kyrgyzstan 2–7 July 2018
http://geoweb.mit.edu/~floyd/courses/gg/201807_Bishkek/
Material from R. W. King, T. A. Herring, M. A. Floyd (MIT) and S. C. McClusky (now at ANU)

## Slide 2: The expectation …
When GPS, Glonass, Beidou, and Galileo are deployed and modernized, there will be > 100 satellites and 12 distinct frequencies available for tracking
Obvious advantages for kinematic positioning and atmospheric studies, but also a means to separate periodic signals due to aliasing in the GPS orbits
Full deployment expected by 2020, but constellations > 20 SVs by late-2018 should provide highly useful results

## Slide 3: Outline
New Global Navigation Satellite System (GNSS) processing capabilities in GAMIT/GLOBK 10.70
Overview and brief description of current GNSS
Basics of how to process GNSS data in GAMIT/GLOBK
  New script options (e.g. sh_gamit)
  Importance of not mixing code releases and updating tables to latest versions
Results of initial tests
Some thoughts on GNSS implementation

## Slide 4: GNSS available in GAMIT/GLOBK
As of GAMIT/GLOBK release 10.70 (2018-06-13), all Global Navigation Satellite Systems (GNSSs) may be processed:
  GPS (USA), BeiDou (China), Galileo (Europe), IRNSS (India), GLONASS (Russia), QZSS (Japan)
GNSS data must be processed separately for each system in GAMIT, i.e. one cannot process GPS data and Galileo data simultaneously

## Slide 5: Why process separately?
  Dual-frequency observations are fundamental for GNSS to remove the ionosphere and are easily implemented under the current structure of GAMIT, but processing different systems across more than two frequencies simultaneously requires a different algorithmic approach and will take some time to implement
  Solution (h-) files from multiple systems (as with multiple sub-nets) can be rigorously combined in GLOBK to estimate site coordinates and velocities for static observations
  Based on research thus far, it is not clear that joint processing will Improve results for the long-sessions used for mm-level measurements, though that may change as the systems mature (improved orbits and knowledge of inter-system signal biases )

## Slide 6: Summary of GNSSs

## Slide 7: What is GPS?
The Global Positioning System is the U.S. global navigation satellite system
Orbital design is medium Earth orbit (approximately 20,200 km) inclined at 55° to equatorial plane
Dual L-band frequencies of 1575.42 MHz (L1) and 1227.60 MHz (L2)
  Modernization has introduced a third L-band frequency of 1176.45 MHz (L5) as well as “civilian” implementations of the original frequencies (L1C and L2C)
http://www.gps.gov/

## Slide 8: What is GLONASS?
GLONASS is the Russian global navigation satellite system
Global constellation launched from 1982 and nominally but never realistically operational from 1993; revamped with new satellites from 2003
Similar to GPS (and Galileo and BeiDou-2) in orbit geometry
  Main orbital design is 3 medium Earth orbital planes (approximately 19,100 km) inclined at 64.8° to equatorial plane (24 satellites)
Differs primarily in using different frequencies rather than different codes to distinguish satellites – complicating the observation equations and making ambiguity resolution more difficult
https://www.glonass-iac.ru/en/

## Slide 9: What is Galileo?
Galileo is the European navigation satellite system
Global constellation launched from 2007, currently operational and due to be fully completed by 2020
Mostly similar to GPS (and GLONASS and BeiDou-2)
  Orbital design is 3 medium Earth orbital planes (approximately 23,222 km) inclined at 56° to equatorial plane
  Triple frequencies of 1575.42 MHz (E1), 1191.795 MHz (E5) and 1287.75 MHz (E6) (cf. 1575.42 MHz and 1227.60 MHz for GPS)
http://www.esa.int/Our_Activities/Navigation/Galileo

## Slide 10: What is BeiDou?
BeiDou (BDS) is the Chinese navigation satellite system
Global constellation (BeiDou-2 or COMPASS) launched from 2007, currently operational and due to be fully completed by 2020
Mostly similar to GPS (and GLONASS and Galileo)
  Main orbital design is medium Earth orbit (approximately 21,528 km) inclined at 55° to equatorial plane (27 satellites)
  Other satellites in geostationary (5) and inclined geosynchronous (3) orbits (approximately 35,786 km)
  Dual frequencies of 1561.098 MHz (C2) and 1207.140 MHz (C7) (cf. 1575.42 MHz and 1227.60 MHz for GPS)
http://en.beidou.gov.cn/

## Slide 11: What is IRNSS (or NavIC)?
The Indian Regional Navigation Satellite System (or Navigation with Indian Constellation) is a hybrid navigation satellite system
Currently seven satellites (3 geostationary plus 4 geosynchronous)
  However, all three rubidium atomic clocks on satellite IRNSS-1A were announced to have failed in the latter half of 2016
Probably only useful over surroundings of Indian Ocean
From http://www.isro.gov.in/irnss-programme

## Slide 12: What is QZSS?
The Quasi-Zenith Satellite System is Japan’s high-altitude navigation satellite system
  Designed to augment GPS, not replace it
Currently only one operational satellite
  Planned to become four by end of 2018 and ultimately seven
Probably only useful for western equatorial Pacific
http://gzss.go.jp/en/
From http://qzss.go.jp/en/overview/services/sv02_why.html

## Slide 13: Processing GNSS in GAMIT/GLOBK

## Slide 14: Version awareness and warnings
A major change between GAMIT/GLOBK 10.5 and 10.6 was the format of many tables (e.g. dcb.dat, svnav.dat, etc.) to accommodate code changes for GNSS
GAMIT/GLOBK 10.61 and 10.70 built upon the new file structures to deliver the data processing capability
Given these major changes, many tables used in GAMIT/GLOBK 10.6, 10.61 and 10.70 are not backwards compatible with GAMIT/GLOBK 10.5 and prior releases
You cannot use many tables that came with GAMIT/GLOBK 10.5 and prior to process (GPS-only or GNSS) data using GAMIT/GLOBK 10.6 and later
Notes: Instead of the old scheme in which satellite names were based on the PRN number, with the SV number carried along, with the new files, the satellites are ordered by SV number (generally the launch order) and identified for modeling by their spacecraft body names (see svnav.dat0

## Slide 15: Suggestions for processing strategies
If you wish to combine data from different GNSS, process each system in a separate experiment directory, e.g. /2017G and /2017E for GPS and Galileo
Download the RINEX files in advance to check for availability of GNSS signals
For sh_gamit use the “-gnss” option to specify the GNSS and “-orbit codm” (“-orbit igsf” OK for GPS)
Check the orbit-fit rms files in the /igs directory to assess the orbit quality
Combine the resulting h-files in GLOBK to produce a single result (time series or velocities)

## Slide 16: RINEX files
RINEX 2, which is still by far the most common format of RINEX file, was designed in an era when only GPS was viable for observation
Since the redesign of GPS to broadcast a second code on L2 (“L2C”) specifically for civilian use, the restoration of GLONASS and the introduction of other navigation satellite systems, RINEX 2 no longer suffices to track all available observations
Be very careful with how you translate and use other people’s RINEX 2 files with L2C (see Berglund et al., 2010; Blume et al., 2012; and http://kb.unavco.org/kb/article/the-effects-of-l2c-signal-tracking-on-high-precision-carrier-phase-gps-postioning-689.html)

## Slide 17: GAMIT
Several scripts now have an additional option (“-gnss”) that sets the type of GNSS
  Most likely to use directly: sh_gamit, sh_get_orbits, sh_sp3fit
  Less likely to use directly: sh_preproc, sh_bcfit, sh_rxscan, sh_get_times, sh_makexp
Valid arguments are (only one of)
  G (GPS)
  R (GLONASS)
  C (BeiDou-2/COMPASS)
  E (Galileo)
  J (QZSS)
  I (IRNSS)
The default is still “G” (GPS)

## Slide 18: GLOBK
GLOBK should work in the normal manner with either baseline or relax mode (orbits estimated). Processing in relax mode allows the orbits to be fixed later in GLOBK which will generate a solution equivalent to baseline mode processing.
Satellite naming scheme has changed to accommodate GNSS (htoglb lists). The default in GLOBK processing is currently to retain the GPS names as PRN_xx (see globk.hlp and USE_PRNN command).
See GLOBK lectures, including those on creating time series using glred and combination or velocity solutions using globk

## Slide 19: track
track, the kinematic processing module, is not yet capable of reading RINEX 3 files or using GNSS data other than GPS
Development to incorporate
  However, the same inter-system bias, memory and computing time limitations exist for track as for GAMIT, so be aware of this one the capabilities are coded and released

## Slide 20: Results of initial tests
Systems processed:
GPS (L1 and L2)
Galileo (E1 and E5)
BeiDou (C2 and C7)
5 days processed (2017-121 to 2017-125)
Notes: To test that the current code runs smoothly and produces results comparable to the quaility of existing orbits, we processed GPS, Galileo, and Beidou observations over 5 days from 15 stations that are producting RINEX 3 files containing the two primary frequencies from each of these systems. We assessed the orbit quality from the agreement among IGS Acs submitting solutions and the satellite later ranging residuals for Galileo and BeiDou. Roughly speaking the Galileo and Beidou orbits are factors of 2-4 worse than GPS and at the level of 2-3 ppb. The effect of orbit errors on site coordinates depends on the number of satellites (next slide)

## Slide 21: Sky tracks Day 121 at Spanish site VILL Each circle covers a 4-hr window
GPS
Galileo
Beidou
Notes: GPS has 32 SVs tracked; Galileo 18; Beidou 8 (3 MEO and 5 geostationary)

## Slide 22: Phase RMS (for 2017-121)
From sh_gamit_121[gec].summary (mm):
Site | GPS | Galileo | BeiDou
ASCG | 7.8 | 9.1 | 4.8
BOR1 | 5.6 | 5.9 | 6.7
BRST | 8.5 | 9.7 | 7.0
BRUX | 4.4 | 5.0 | 4.7
DJIG | 5.9 | 8.0 | 17.1
GANP | 5.9 | 6.6 | 8.4
KIRU | 6.8 | 8.0 | 10.7
KOUR | 10.6 | 12.6 | 5.5
Site | GPS | Galileo | BeiDou
LAMP | 4.5 | 6.2 | 6.2
MAL2 | 7.7 | 10.0 | 12.7
MAS1 | 7.1 | 8.1 | 3.1
NICO | 6.1 | 9.1 | 22.1
REYK | 8.4 | 11.1 | 8.3
STJ3 | 5.3 | 6.0 | 2.3
VILL | 8.1 | 9.6 | 5.1
ALL | 7.1 | 8.6 | 11.3
Notes: The Galileo phase noise is slightly larger than GPS at each station, possibly due to antenna mistuning for E5 or poorer orbits. Beidou shows a much larger variation because only three MEOs were tracked.

## Slide 23: Ambiguity resolution
Best from sh_gamit_<DDD>[gec].summary:
System | Wide lane (WL) | Narrow lane (NL)
GPS | 98% | 91%
Galileo | 99% | 78%
BeiDou | 80% | 50%
Notes: The same factors that contributed to the larger phase noise likely also cause the degradation of ambiguity resolution for Galileo and Beidou

## Slide 24: Time series stabilization
From “POS STAT” lines in .org-file(s) (mm:
System | Sites | E | N | U
GPS | 10 | 1-2 | 1–2 | 6–10
Galileo | 9-10 | 2-3 | 2–4 | 11-16
BeiDou | 6–9 | 1–7 | 3–9 | 6–18

## Slide 25: Example time series
GPS
Galileo
BeiDou

## Slide 26: Example time series
GPS
Galileo
BeiDou
Notes: 5-day scatter for station BOR1 in centrl Europe. For the full set of 15 stations, the wrms N, E, U was
0.3-2.9, 0.2-2.4, 2-10 mm for GPS, 0.3-2.8, 0.3-2.4, 6-20 mm for Galileo, and 3-72, 5-66, 6-120 mm for Beidou.

## Slide 27: Example time series
GPS
Galileo
BeiDou

## Slide 28: Example time series
GPS
Galileo
BeiDou

## Slide 29: Example time series
GPS
Galileo
BeiDou

## Slide 30: Example time series
GPS
Galileo
BeiDou

## Slide 31: Example time series
GPS
Galileo
BeiDou

## Slide 32: Example time series
GPS
Galileo
BeiDou

## Slide 33: Example time series
GPS
Galileo
BeiDou

## Slide 34: Example time series
GPS
Galileo
BeiDou

## Slide 35: Example time series
GPS
Galileo
BeiDou

## Slide 36: Example time series
GPS
Galileo
BeiDou

## Slide 37: Example time series
GPS
Galileo
BeiDou

## Slide 38: Example time series
GPS
Galileo
BeiDou

## Slide 39: Example time series
GPS
Galileo
BeiDou

## Slide 40: Position differences (GPS versus Galileo)
Notes: The wrms differences are 2.0 mm in N and 1.2 mm in E, with the stations near the centroid of the network generally (but not uniformly) better than those on the periphery, presumably reflecting orbital errors.

## Slide 41: Initial impressions
Galileo has robust phase tracking and could, for small regional networks with good satellite coverage, now produce nearly GPS-quality results
The Beidou constelletion will need to be filled out significantly, expected by mid-2018
BeiDou also appears to be prone to single cycle slips, resulting in poor detection and cleaning of tracked phase
  This may be improved by tuning autcln.cmd

## Slide 42: Other current limitations to GNSS
Antenna phase center offsets (PCOs) and variations (PCVs) for frequencies other than GPS’s L1 and L2 do not have calibrations yet and are not well known
  Affects accuracy of position and may increase phase misfit as a function of elevation and azimuth

## Slide 43: Future developments
In addition to multi-GNSS data, the GPS system (and Galileo) now has many satellites that broadcast on three frequencies (L1, L2 and L5)
This creates the possibility of forming two additional types of linear combination (L1/L5 and L2/L5) beyond the usual LC (L1/L2)
Since the formation of the linear combination is a way to minimize the effect of the ionosphere,

## Slide 44: Current limitations of GAMIT
Although GAMIT does have the ability to read RINEX 3 files, they must be named according to the RINEX 2 file naming convention in the rinex/ directory to be included in processing (see sh_rename_rinex3)
  i.e. ssssdddi.yyo where “ssss” is four-character site ID, “ddd” is ordinal date (day-of-year), “i” is session index and “yy” is two-digit year
Only dual (constant) frequency observations may be processed at any one time

## Slide 45: Summary
GAMIT/GLOBK is now (as of 10.70) capable of processing all GNSS data
GNSS data are available but few users are actually collecting or processing such data
As a result, global orbits are poorly constrained by ground stations with accurate coordinates in the terrestrial reference frame
  Satellite orbital models and antenna designs are less well known than GPS
  Many GNSSs other than GPS are in a similar “weak” state to where GPS was in the early 1990s before the advent of the IGS
It is difficult to predict at what time the other systems will enhance rather than degrade GPS results but we should see rapid improvement with the launch of more satellites and the expansion of the tracking network in the next 18 months
Notes: Examination of the differences between analysis centers and comparison with SLR range residuals suggests that Glonass, Beidou, and Galileo orbits are about a factor of 2-4 worse than those for GPS.

## Slide 46: References
  Berglund, H., F. Blume, L. H. Estey, and A. A. Borsa (2010), The Effects of L2C Signal Tracking on High-Precision Carrier Phase GPS Positioning, Abstract G11B-0640 presented at 2010 Fall Meeting, AGU, San Francisco, Calif., 13-17 Dec.
  Blume, F., H. Berglund, and L. Estey (2012), The Effects of L2C Signal Tracking on High-Precision Carrier Phase GPS Positioning: Implications for the Next Generation of GNSS Systems, Abstract G52B-07 presented at 2012 Fall Meeting, AGU, San Francisco, Calif., 3-7 Dec. [http://acc.igs.org/trf/agu12_blume_l2c.pdf]
  Berglund, H. (2016), The Effects of L2C Signal Tracking on High-Precision Carrier Phase GPS Postioning, http://kb.unavco.org/kb/article/the-effects-of-l2c-signal-tracking-on-high-precision-carrier-phase-gps-postioning-689.html.
  Estey, L. (2017), Helpful tip of week 1962, https://postal.unavco.org/pipermail/teqc/2017/002316.html.
  Montenbruck, O., R. Schmid, F. Mercier, P. Steigenberger, C. Noll, R. Fatkulin, S. Kogure, and A. S. Ganeshan (2015), Adv. Space Res., 56, 1015–1029, doi:10.1016/j.asr.2015.06.019.