## Slide 1: GLOBK: Combination methods Lecture 03
Thomas Herring
tah@mit.edu

## Slide 2: GLOBK Overview
Here we review the main features of globk and glred.
Topics:
  Program flow
  Kalman filtering
  Globk files and estimation rules
  Glorg progam/function: Define origin plus other things
  Output options
  Flow of programs
  sh_glred: Globk equivalent of sh_gamit

## Slide 3: GLOBK Purpose
GLOBK is a suite of programs designed to combine geodetic results together. GPS phase processing can take a considerable time and GLOBK provides a fast method for make large network solutions, combining many days to years of data together and studying alternative parameterization and reference frames for the velocities of sites.
GLOBK uses as data input, quasi-observation files called binary h-files which contain geodetic solutions with loosely constrained full covariance information. These files can generated from gamit solutions or SINEX files.
GLOBK is a smoothing Kalman filter and can incorporate random walk process noise in its estimation (method for accounting for temporally correlated noise in time series).
Its two main uses are to generate velocity field estimates and time series in a well-defined and often different reference frames. (It can also be used to merge large networks of GPS sites).

## Slide 4: Common applications of GLOBK
Repeatability analysis ( glred )‏
  individual sessions
  combine regional and global files for orbit control and reference frame (orbit control is not so important anymore; IGS orbits are very good apriori)
Combine sessions to get average position over survey
  connects stations observed separately
  reduces number of h-files to be used for velocities
Combine averaged positions to estimate velocities
  and/or earthquake offsets and post-seismic motion
Notes: 4

## Slide 5: GLOBK Function and File Flow
htoglb: Translate GAMIT h-files to (e.g., hemeda.10256 ) to globk
h-files (e.g. h1009131200_emed.glx
[h-file list].gdl 
globk_comb.cmd
Itrf08.apr
IGS08_101117.eq
g
l
o
b
k
   globk_comb.prt
  globk_comb.log
comb.com (binary solution file that can be used in glorg)
comb.com 
glorg_comb.cmd
itrf08.apr
stab_site [list]
globk_comb.org
g
l
o
r
g
Names of files here can be chosen arbitrarily.
Notes: 5
This flow chart shows the primary control files needed to run globk and glorg. The (ascii) h-file written by GAMIT and translated to a (binary) globk h-file by htoglb is loosely constrained, so the print (.prt) file written by globk is not a meaningful basis for evaluating the results. The log file, however, gives the chi2 increments if more than one h-file is input to globk. The loosely constrained solution (now comb.sol) output by globk is read by glorg and put into a meaningful reference frame using generalized constraints. The glorg print file (globk_comb.org) is the primary out to be examined.

## Slide 6: GLOBK file name conventions
GLOBK uses arbitrary file names but there are some conventions used:
  Binary h-files from htoglb: .glx is bias fixed, .glr is bias free (normally not used)
  List of binary h-files to process: .gdl extent
  GLOBK and GLORG command files: globk_<type>.cmd and glorg_<type>.cmd
  Output files: print file (no glorg reference frame) .prt (often not output); glorg output .org; log file .log
  Apriori coordinate files: .apr
  Earthquake and rename file: .eq
  Lists of stabilization sites (used with source command): .stab

## Slide 7: Kalman Filtering
Equivalent to sequential least-squares estimation but allowing for stochastic processes, usually a 1st-order Gauss-Markov process
GLOBK allows a random walk for coordinates, EOP, network translation and scale, and satellite parameters; variance grows linearly with time
Because a Kalman filter works with covariance matrices (rather than normal matrices), all parameters must have a priori constraints (usually loose)‏
See Herring et al. [1990] and Dong et al. [1998] for a more thorough description as applied to geodetic analysis
Notes: 7

## Slide 8: GLOBK Structural Confusions
globk and glred are the same program with (slightly) different ways of treating the h-file ( gdl ) list:
  globk: all h-files in combined in a single solution
  glred: each h-file generates a separate solution (unless followed by a + )‏. glred is a small program that generates sub-set .gdl files and runs globk.
Two types of solution files:
  h-files for saving and external exchange (backward compatible)‏
  com/sol file is internal, format changes with versions
glorg called by globk/glred or run separately to apply generalized constraints to solution and estimate plate rotations
Notes: 8

## Slide 9: GLOBK files
User supplied
  command files (may include ‘source’ files)‏
  gdl list of h-files
  binary h-files (created from SINEX or GAMIT h-)‏
  apr file(s) (optional but recommended)‏
  EOP (in_pmu file, optional but recommended)‏
  eq_file (optional, but must appear at top)‏
Generated by globk
  srt, com, sol , svs (must be named and come first)‏
Output files
  screen, log, prt, org and output h-file
Notes: 9

## Slide 10: GLOBK file handling
log, prt, org files are concatenated, so should be removed or renamed unless you want them together (e.g. glred)‏. The ‘eras’ option can be used in the prt_opt and org_opt command in the globk command file to erase these files (should not be used with glred).
com, srt, sol files are overwritten; com/sol should not be renamed since the original sol file name is imbedded in the com file
Automatic naming using wild-cards is available for com, srt, sol, org, and output h-files (i.e., name used depends on name of .gdl file; needed for parallel processing.)
Notes: 10

## Slide 11: Estimation commands rules
For a parameter to estimated in globk, apr_xxx command must be used where xxx is a parameter type (e.g., neu, svs, wob, ut1, atm)‏
If a parameter is not mentioned, it does not appear in the solution, but if it appears in the h-file (i.e, estimated in GAMIT), its uncertainty is implicit in the globk solution; e.g., if orbits are estimated in GAMIT and you want them constrained in globk, use apr_svs. If apr_svs is not used, orbits are left constrained.
If zero given as a priori sigma, then parameter is not estimated (effectively left unconstrained)‏
To force a parameter to it’s a priori value, use F as the a priori sigma
Parameters estimated in glorg must be kept loose in globk ; if rotation or scale is not estimated in glorg, it must be tightly constrained in globk
Notes: 11

## Slide 12: Earth Orientation Parameters ( EOP )
Normally used in two forms:
  Global network of stations (allows rotation in glorg)‏
    apr_wob 10 10 1 1
    apr_ut1 10 1
  Regional network (constrained). When constrained this way system is not free to rotate so xrot, yrot, zrot should not be used in pos_org command( see pos_org in glorg )‏
    apr_wob .2 .2 .02 .02
    apr_ut1 .2 .02
In many analyses, the global form is used even for regional networks in order to allow rotation estimation in glorg. (Care is needed if network is not not surrounded by stations with well defined motions).
When using BASELINE option in gamit sestbl. apr_wob and apr_ut1 must be used to allow rotations. For multiday sessions, mar_wob and mar_ut1 should also be used.
Notes: 12

## Slide 13: Data Editing
To account for temporal correlations in time series we typically use random-walk (RW) process noise with the mar_neu command (units m2/yr )‏
Typical values are 2.5E-8 (0.5 mm in 1 yr) to 4E-6 (2 mm in 1 yr)
  mar_neu all 2.5E-8 2.5E-8 2.5E8 0 0 0
  mar_neu chdu 4E-6 4E-6 4e-6 0 0 0
The sh_gen_stat command can used to generate process noise estimates provided sufficiently large number of position estimates are available.
To down-weight noisy segments or equalize continuous and survey-mode data in a combined h-file, can add random noise (units are m)‏
  sig_neu all .001 .001 .003
  sig_neu ankr .005 .005 .020 2002 10 1 0 0 2002 11 30 24 0
  sig_neu EMED0504 .010 .010 .1
To remove an outlier, can down-weight severely or rename
  sig_neu ankr .1 .1 .1 2002 10 1 0 0 2002 10 1 24 0
  rename ankr_gps ankr_xcl 2002 10 1 0 0 2002 10 1 24 0 ( eq_file )

## Slide 14: GLORG
Invoked by globk to apply generalized constraints after h-files are stacked and loose solution performed; can be run as a separate program using the com/sol files from globk
Also allows linking of parameters and estimation of Euler poles
Parameters estimated in glorg must be kept loose in globk (coodinates, EOP, scale)‏
GLORG is used to define and refine the reference frame for GLOBK solutions.
Notes: 14

## Slide 15: Invoking GLORG from globk command file
The globk command file contains commands that cause glorg to run when globk completes the solution combination:
  org_cmd < glorg command file name > ---invokes glorg
  org_opt < options for output >
  org_out < output file name >: Normally not used because name will be generated from prt file name in the globk runstring.
If org_out is not given then the extent on the print file name is replaced with org
Notes: 15

## Slide 16: GLORG Commands
apr_file – Need not be the same as for globk; needs to contain values only for sites used for stabilization and sites for which coordinates or velocities are equated
pos_org, rate_org – Control what parameters are estimated in stabilization
  xtran ytran ztran – allows translation
  xrot yrot zrot – allows rotation
  scale – allows rescaling of system (if used, estimate scale in globk; apr_scale and possibly mar_scale)‏
cnd_hgtv – Control relative weights of heights (variances, nominally 10 but increasing value will reduce heights effecting horizontal position estimates; 1000 is good for this)‏
stab_ite – # of iterations and sigma-cutoff to remove a site
stab_site – List of sites to use in stabilization

## Slide 17: Controlling Print Output
crt_opt, prt_opt, org_opt specify output options for screen, print and org files
globk/glorg help gives all options, main ones are:
  ERAS -- erase file before writing (normally files appended)‏
  NOPR -- Do not write output ( e.g., for globk when invoking glorg )‏
  BLEN -- Baseline lengths
  BRAT -- baseline rates when velocities estimated
  RNRP -- generates reports on differences in parameter estimates after renames.
  FIXA -- makes apriori coordinates and velocities consistent when equates are used in glorg (can sometimes fail in complicated rename scenarios--best if apr_file is provided with consistent values)‏
  VSUM -- Lat/long summary of velocity (needed to plot velocities)‏
  PSUM -- Lat/long position summary
  GDLF --Include list of hfiles and chi**2 increments from run
  CMDS -- Echos globk command file into output file
Notes: 17

## Slide 18: Handling Steps due to Earthquakes (or instrument changes)
Level 1 ( always necessary )‏
  Rename the site, either automatically (e.g. Wenchuan, May 2008)
  <Code> <Lat> <Long> <Radius> <Depth> <epoch>
  eq_def WC 31.099 103.279 1000 20 2008 5 12 6 28
  eq_rename WC forces rename, e.g. CHDU_GPS --> CHDU_GWC
  eq_cosei to specify spatially dependent constraints on position adjustments
or explicitly (for non-tectonic steps)‏
  rename iisc_gps iisc_1ps 1995 10 1 2 0 0 1999 12 1 5 0
  ! Antenna swap from Trimble SST to AOA choke ring
  rename lake_gps lake_xhi 2002 1 12 0 0 2002 1 12 24 0
Commands put in the eq_file (not globk command file)
Effect is to make the site’s coordinates and velocities independent in the solution
The script sh_makeeqdef can be used to generate an eq definition file bases on the NEIDC seismic catalog and program stinf_to_rename can used to generate renames due to antenna changes.

## Slide 19: Handling Steps due to Earthquakes (or instrument changes)
Level 2 ( almost always desirable )‏
In glorg equate the velocities, either explicitly
  equate iisc_gps ndot iisc_1ps ndot
  equate iisc_gps edot iisc_1ps edot
  equate iisc_gps udot iisc_1ps udot
or automatically
  eq_dist 1000 ndot
  eq_dist 1000 edot
  eq_dist 1000 udot
  unequate chdu_gps ndot chdu_gwc ndot
  unequate chdu_gps edot chdu_gwc edot
  unequate chdu_gps udot chdu_gwc udot
Effect is to (re)link the adjustment (should be used with the FIXA option)
Can create a soft link with “constrain” command (so that values are not forced to be exactly the same.
Equates are applied to adjustments to apriori coordinates, so in general these should be the same (FIXA option will often do this automatically; unify_apr is another method).

## Slide 20: Handling Steps due to Earthquakes (or instrument changes)
Level 3 ( often useful to improve far-field velocities )‏
Equate the positions when a site within the EQ radius has a small displacement
  equate xian_gps npos xian_gwc npos
  equate xian_gps epos xian_gwc epos
  equate xian_gps upos xian_gwc upos
May be used in conjunction with a model, applied as an offset in a rename command (need to be very careful with approach or offsets can applied multiple times).
  rename xian_gwc xian_gwc 2008 5 12 6 28 -0.003 0.004 0.001 NEU
Offsetting the coordinates in the globk apr_file

## Slide 21: Program Flow
Read all the h-file headers to determine their contents ( sites, other parameters, epoch range)
Apply renames as requested in the eq_file
Sort the h-file list forward or backward in time ( srt_dir )
Initialize the Kalman filter with the a priori constraints ( apr_xxx )‏
Read in the h-files, one at a time, compute the chi2 increment, coordinate adjustment, and rotation implied by the new data; if within tolerance (max_chii ), update the solution and write the chi2 increment to the log file
Write the solution to the sol_file and prt file (and optionally to a new h-file)‏
Optionally invoke glorg to apply generalized constraints
  Apply the constraints ( iterative “stabilization” )‏
  Apply linkage of parameters ( equate, constrain, force ), computing the chi2 increment for each
  Estimate plate rotations ( plate command )
  Write the solution to the org file ( glorg prt file )
Notes: 21

## Slide 22: Things GLOBK cannot do
Repair mistakes in original analysis
  cycle slips
  wrong antenna phase center models
Resolve ambiguities
  (would make files too large)‏
Overcome non-linear effects
  As in GAMIT, adjustments must be less than ~ 30 cm
But GLOBK can delete stations
  can help avoid contaminating solution
Notes: 22

## Slide 23: Apr Files in GLOBK Processing
GAMIT
  10 m accuracy for all sites for cycle-slip repair
  < 30 cm final adjustment for linearity (1st solution guarantees)‏
  ~5 cm accuracy in constrained site(s) for ambiguity resolution
globk
  If invoking glorg for reference frame, apr_file usually optional in globk
  If not invoking glorg, need accurate apr_file entries for constrained sites
  For complicated renames and equates, apr_file may be needed in globk
glorg
  Apr_file needs coodinates only for reference sites and equates
Notes: 23

## Slide 24: What can go wrong ?
globk
  H-files not used: removed automatically for high chi2, coordinate adjustment, or rotation ( max_chii command )‏
  High chi2 increment: inconsistent data
  Station “missing”: not present in h-file or renamed out ( use glist )‏
glorg
  Stabilization fails: too-few sites in stabilization
  Large uncertainties: poor stabilization
  Too-small uncertainties for some stabilization sites: rotation parameters absorbing coordinate adjustment
  High chi2 in equate: inconsistent data
  Wrong velocity for equated sites: unmatched apriori

## Slide 25: Associated programs
  htoglb – Translates various ascii solution files into GLOBK h-files (GAMIT h-files, SINEX)
  glbtosnx -- Generates SINEX files from binary h-files
  glist -- lists the contents of a series of h-files
  hfupd -- Updates binary h-files for changes in station.info or sinex header file (distributed by IGS)‏
  ensum, enfit, tscom, tsfit -- time series analysis (batch)
Matlab derived programs (interactive):
  velview -- displays and analyzes velocity fields
  tsview -- displays and analyses time series.
Notes: 25

## Slide 26: sh_glred script
A convenient way to run globk/glorg to generate time series: sh_glred –s 2011 256 2011 303 -opt H G E
Requires user-constructed command files in /gsoln (globk_comb.cmd and glorg_comb.cmd : eq_file, apr_file, use_site list, stab_stie list, .. ) Copy templates from gg/tables and edit for your network.
Automatically creates one gdl file per day (unlike glred when run directly, which may have a single gdl file with h-files for many days
With the ‘E’ option, will invoke sh_plotcrd (calling ‘ensum’) to extract coordintes from the org files and plot them.
Additional options allow automatic download of global h-files from MIT or SOPAC and combination with the local h-files
Notes: 26

## Slide 27: Suggested Directory Structure for Multi-year Processing
/project
/YYY1 /YYY2 . . . /vsoln /tables
/tables /gsoln /DDD . . .
Notes
• Experiment/project directory names do not have to match the sh_gamit 4-character expt name
• Experiment-wide tables ( e.g. apr, eq/rename, use_site, edit files ) may reside in top-level or yearly /tables (just get the path right in the globk/glorg command files)‏
• Can add multiple ‘solution’ directories at the top level for different analyses
• Copy templates for globk_vel.cmd and glorg_vel.cmd from gg/tables to /vsoln and edit
• Generate h-file list in /vsoln using, .e.g. ‘ ls YYY?/gsoln/h*glx > project.gdl ‘
Notes: 27

## Slide 28: Steps in Multi-year Analysis
Generate daily time series for each year or partial year using sh_glred ; create edit commands as appropriate (sig_neu and/or xcl renames)
Optionally aggregate the days into weekly, monthly, or survey-length H-files using sh_glred with the –ncomb option and out_glb specified in globk_comb.cmd.
Generate a multi-year time series using glred/glorg and sh_plotcrd; repeat with reweighting
Perform a velocity solution using globk/glorg; plot with sh_plotvel
Extract a new stabilization apr file from the velocity solution
Repeat the multi-year time series using the new apr file and a stab_site list expanded to include all well-determined CGPS and SGPS sites
Note: It may be convenient to use the ‘source’ option in globk_comb.cmd and globk_vel.cmd to include use_site, stab_site, and sig_neu lists (see templates)
Notes: 28

## Slide 29: GLOBK Commands for Multi-year Solutions
In /voln directory:
Repeatabilities
  glred 6 globk.comb.prt globk.comb.log project.gdl globk_comb.cmd
  sh_plotcrd –f globk_comb.org –s long
Velocities
  globk 6 globk_vel.prt globk_vel.log project.gdl globk_vel.cmd
  sh_plotvel -f globk_vel.org -R244.5/25140.5/46.5

## Slide 30: Eq_file entry for Maule earthquake
* EQ_DEF M 8.8 eq_def MA -36.030 -72.850 3539.0 26.0 2010 2 27 6 34 190.4683 eq_rename MA eq_coseis MA 0.001 0.001 0.001 190.468 190.468 190.468 eq_log MA 1.0 0.001 0.001 0.001 190.468 190.468 190.468
(or ftp the file Maule.eq from chandler.mit.edu, (mitg) dd incoming/lima )

## Slide 31: Convenient Methods of Creating Edit Commands
To eliminate a data point (station/epoch), you can put into the eq_file commands of the form
rename areq areq_xcl 2009 3 5 0 0 2009 3 5 24 0
which you can create with a specified sigma-cutoff in tsview (interactive) or tsfit (batch); you can also create the commands with a mouse click in tsview
To downweight horizontal and/or vertical data points (station/epoch), you can put into the globk command file (perhaps using ‘source daily.reweights’) commands of the form
sig_neu areq 0.010 .010 .100 2009 3 5 0 0 2009 3 5 24 0
which you can create with a few keystrokes by using program grw
grw areq 09 64 64 10 100
(day 64 is 5 March; units here are mm, but m in sig_neu)
( ‘grw’ stands for ‘globk reweight’. It appends to a file temp.out )
NOTE: If you are referencing a combined h-file (more than 1 day), the date range given for the rename or sig_neu command must encompass the range of the h-file times.

## Slide 32: Summary
GLOBK has many features and due to its evolution, there are often multiple ways of doing the same or similar things.
There is extensive help in the ~/gg/help/ directory and discussion in the documentation.
GLOBK is where all the major analysis decisions are made and hence can be quite complex for large analyses.
Experimentation and testing your ideas of how different options effect the results is one the best ways to learn the software (e.g., what happens to position/velocity estimates if the apr_tran command is added to the globk command file? How do my estimates and uncertainties change if the apr_neu and mar_neu commands are changed?